## DMX-protocol

Control channel 1 - Gobo-wheel, gobo-shake

| DMX-value | Feature |
| --- | --- |
| 0-5 | Blackout |
| 6-31 | Strobe-effect |
| 32-41 | Open |
| 42-52 | Gobo 1 |
| 53-63 | Gobo 2 |
| 64-73 | Gobo 3 |
| 74-84 | Gobo 4 |
| 85-95 | Gobo 5 |
| 96-105 | Gobo 6 |
| 106-116 | Gobo 7 |
| 117-127 | Gobo 8 |
| 128-137 | Gobo 9 |
| 138-147 | No function |
| 148-155 | Gobo 1 shake with increasing speed |
| 156-163 | Gobo 2 shake with increasing speed |
| 164-171 | Gobo 3 shake with increasing speed |
| 172-179 | Gobo 4 shake with increasing speed |
| 180-187 | Gobo 5 shake with increasing speed |
| 188-195 | Gobo 6 shake with increasing speed |
| 196-203 | Gobo 7 shake with increasing speed |
| 204-210 | Gobo 8 shake with increasing speed |
| 211-217 | Gobo 9 shake with increasing speed |
| 218-223 | Sound-controlled |
| 224-225 | Stop |
| 226-255 | Cont. gobo-wheel rotation with increasing speed |

Control channel 2 - Dimmer intensity

| DMX-value | Feature |
| --- | --- |
| 0-255 | Gradual adjustment of the dimmer intensity from 0 to 100 % |