## DMX-protocol

Control channel 1 - Horizontal movement (Pan) (within 180°)

Push slider up in order to move the mirror horizontally (PAN).

Gradual mirror adjustment from one end of the slider to the other (0-255, 128-center). The mirror can be stopped at any position you wish.

| DMX-value | Feature |
| --- | --- |
| 0-255 | Gradual adjustment of the mirror position from left to right |

Control channel 2 - Vertical movement (Tilt) (within 90°)

Push slider up in order to move the mirror vertically (TILT).

Gradual mirror adjustment from one end of the slider to the other (0-255, 128-center). The mirror can be stopped at any position you wish.

| DMX-value | Feature |
| --- | --- |
| 0-255 | Gradual adjustment of the mirror position from down to up |

Control channel 3 - Colour-wheel

| DMX-value | Feature |
| --- | --- |
| 0-17 | Open/white |
| 18-35 | Red |
| 36-53 | Yellow |
| 54-71 | Violet |
| 72-89 | Green |
| 90-107 | Orange |
| 108-125 | Blue |
| 126-143 | Pink |
| 144-161 | Light green |
| 162-179 | Light blue |
| 180-197 | Orange/yellow |
| 198-215 | Light yellow |
| 216-233 | Magenta |
| 234-251 | Bi-colour-filter (red with blue) |
| 252-255 | Bi-colour-filter (yellow with green) |

Control channel 4 - Gobo-wheel

| DMX-value | Feature |
| --- | --- |
| 0-17 | Open |
| 18-35 | Gobo 1 |
| 36-53 | Gobo 2 |
| 54-71 | Gobo 3 |
| 72-89 | Gobo 4 |
| 90-107 | Gobo 5 |
| 108-125 | Gobo 6 |
| 126-143 | Gobo 7 |
| 144-161 | Gobo 8 |
| 162-179 | Gobo 9 |
| 180-197 | Gobo 10 |
| 198-215 | Gobo 11 |
| 216-233 | Gobo 12 |
| 234-251 | Gobo 13 |
| 252-255 | Gobo 14 |

Control channel 5 - Shutter, strobe

| DMX-value | Feature |
| --- | --- |
| 0-14 | Shutter closed |
| 15 | Open |
| 16-250 | Strobe-effect with increasing speed |
| 251-255 | Open |