## DMX-protocol

Control channel 1 - Horizontal movement (Pan) (within 180°)

Push slider up in order to move the mirror horizontally (PAN).

Gradual mirror adjustment from one end of the slider to the other (0-255, 128-center). The mirror can be stopped at any position you wish.

| DMX-value | Feature |
| --- | --- |
| 0-255 | Gradual adjustment of the mirror position from left to right |

Control channel 2 - Vertical movement (Tilt) (within 90°)

Push slider up in order to move the mirror vertically (TILT).

Gradual mirror adjustment from one end of the slider to the other (0-255, 128-center). The mirror can be stopped at any position you wish.

| DMX-value | Feature |
| --- | --- |
| 0-255 | Gradual adjustment of the mirror position from up to down |

Control channel 3 - Colour-wheel

| DMX-value | Feature |
| --- | --- |
| 0-31 | Open/white |
| 32-63 | Red |
| 64-95 | Yellow |
| 96-127 | Violet |
| 128-159 | Green |
| 160-191 | Orange |
| 192-223 | Blue |
| 224-255 | Pink |

Control channel 4 - Gobo-wheel

| DMX-value | Feature |
| --- | --- |
| 0-31 | Open |
| 32-63 | Gobo 1 |
| 64-95 | Gobo 2 |
| 96-127 | Gobo 3 |
| 128-159 | Gobo 4 |
| 160-191 | Gobo 5 |
| 192-223 | Gobo 6 |
| 224-255 | Gobo 7 |

Control channel 5 - Shutter, strobe

| DMX-value | Feature |
| --- | --- |
| 0-14 | Shutter closed |
| 15 | Open |
| 16-250 | Strobe-effect with increasing speed |
| 251-255 | Open |

Control channel 6 - Rotating gobo index, gobo rotation

| DMX-value | Feature |
| --- | --- |
| 0-4 | Gobo indexing |
| 5-120 | Forwards gobo rotation with decreasing speed |
| 121-139 | No rotation |
| 140-255 | Backwards gobo rotation with increasing speed |